## Slide 1: Week 3: Coding Day
“Teamworking and Collaborative Learning”

## Slide 2: Instruction
Student must complete the Week 3 Coding Day Challenges on USART and I2C for exam revision and the AMR project development.
Develop STM32F446 code to acquire real-time data from the RPLidar C1 and MPU6500 using interrupts, DMA, and relevant peripheral register configuration.
Use PulseView to analyse the sensor signals and protocols, and convert captured data into meaningful physical values.
The minimum required analysis is the revision for final closed-book examination reviewion, namely RPLidar C1 SCAN mode and MPU6500 gyroscope transactions.
Additional extension work should include RPLidar C1 Express mode and the MPU6500 accelerometer are required for the AMR project development.
Submit an analysis report and demonstrate the working system to the TA. The Coding Day mark will be awarded individually through questioning based on the report, the protocol analysis, and the live demonstration.
Submit report using this QR code

## Slide 3: Task 1: STM32F446 Real-Time Sensor Interfacing
Develop an integrated STM32F446 code to acquire data from:
  RPLidar C1 using USART
  MPU6500 using I2C
Your implementation must use a real-time interrupt and DMA approach, not simple polling. This includes configuring the relevant peripheral registers as appropriate, such as:
  USART configuration registers for baud rate and communication setup
  I2C configuration registers for master communication
  DMA stream/channel configuration
  interrupt enable and NVIC configuration
Your code should demonstrate that the microcontroller can continuously receive or transfer sensor data reliably in real time.

## Slide 4: Task 2: Protocol Analysis Using PulseView
Using PulseView logic analyser to capture and analyse the signalling and protocol communication of both RPLidar C1 and MPU6500 sensors.
Your analysis must include the minimum required parts listed in the following sub-sections of RPLidar C1 and MPU6500, which are based directly on the knowledge required for final closed-book examination, together with additional extension analyses towards the project development.
Pulseview Signaling and Protocol Analyses

## Slide 5: Task 2.1: RPLidar C1 Analysis
Capture and analyse the UART communication between the STM32F446 and the RPLidar C1.
Minimum required analysis
  Configure the USART communication settings used for the sensor
  Identify the response descriptor in SCAN mode
  Identify the start of each measurement sample
  Explain how the start bits work in the SCAN-mode packet format
  Decode at least one measurement sample
  Determine and explain:
    whether the sample is valid
    the quality value
    the angle in degrees
    the distance in mm
Additional extension analysis
  Express mode packet structure and behaviour;
  How Express mode differs from normal SCAN mode
  How the captured bytes would be interpreted in Express mode

## Slide 6: Task 2.1: RPLidar C1 Analysis

## Slide 7: Task 2.1: RPLidar C1 Analysis

## Slide 8: Task 2.2: MPU6500 Analysis
Capture and analyse the I2C communication between the STM32F446 and the MPU6500.
Minimum required analysis
  Identify the device address and the meaning of the read/write address bytes
  Identify the register address used in the transaction
  Explain the I2C transaction sequence, including:
    START, address + write, register selection, repeated START, address + read, returned data bytes, ACK/NACK and STOP
  Reconstruct the returned gyroscope values from the captured bytes
  Convert the raw gyroscope readings into:
    16-bit hexadecimal values
    signed decimal values
    physical values in appropriate units
Additional extension analysis
  the accelerometer registers and read sequence
  reconstruction of raw accelerometer output data
  conversion of accelerometer readings into meaningful physical values

## Slide 9: Task 2.2: MPU6500 Analysis

## Slide 10: Task 2.2: MPU6500 Analysis

## Slide 11: Task 3: Analysis Report
Prepare a short analysis report that clearly documents:
  Your peripheral configuration approach
  How interrupts and DMA are used
  PulseView captures of UART and I2C transactions
  Protocol interpretation for each sensor
  Example calculations showing how raw bytes are converted into meaningful values
  Brief explanation of any implementation issues, debugging steps, or limitations
The report should be technical, concise, and structured clearly enough that each member can explain it confidently.

## Slide 12: End of Week3